## Slide 1: Intro to Circuits
Sean Murphy
Tampa Hackerspace
http://goo.gl/e97Eep

## Slide 2: Water Analogy
Electricity is like water flowing through a series of pipes and other elements (like pumps et al.)
Electricity is actually energy from the build-up or movement of charges (usually electrons)

## Slide 3: Voltage – the potential to move charge
Water pressure – Volts (V)
Voltage is the capability to produce current (flow)
A battery is a constant-pressure pump

## Slide 4: Current – the flow of charge
Water flow – Amperes (Amps) (A)
Current will only flow when there is a voltage (pressure) and a non-restricted path
A battery provides current when a load is connected across it

## Slide 5: Power – the expenditure of energy
Pressure*flow
P=V*I
Watts (W)
Power of a component is equal to the product of current through the component and the voltage drop across the component

## Slide 6: Resistance
A small diameter pipe will require a higher pressure to produce the same flow as in a large pipe. There will be a lower pressure at the output compared to the input.
Resistance is the proportion of voltage to current. V=I*R (Ohm’s Law)
Ohms (Ω)

## Slide 7: Adding Resistance

## Slide 8: The simplest of circuits

## Slide 9: Voltage Divider

## Slide 10: Pullup Resistors

## Slide 11: Generic case
Used for simply stepping down voltage
Be careful, this assumes that no current comes out of the center node

## Slide 12: Capacitance
A water balloon on a pipe will inflate to match the pressure of the pipe then expel its contents when external pressure is reduced.
A capacitor holds an electrical charge and provides or accepts current to maintain a potential
Farads (F) F=A*s/V

## Slide 13: Adding Capacitance
Opposite of resistors
Parallel is the sum of individual capacitors
Series is the reciprocal of the sum of reciprocals

## Slide 14: Nothing else is simple

## Slide 15: What you need to know about C
Capacitors are used to filter high frequency from low frequency (or Direct Current (DC))
They smooth out fast changes
When dealing with Alternating Current (AC), a capacitor has a reactance X=1/(2πf*C)
So, a high frequencies, capacitors act small resistors, and the smaller the capacitor, the larger the equivalent resistance

## Slide 16: High pass filter

## Slide 17: Inductors
Think of a waterwheel. It will store energy if there is flow then attempt to continue the flow by making a backpressure if external pressure is removed.
Henries (H)
Like capacitors fight changes in voltage, inductors fight changes in current
X=2πf*L

## Slide 18: Uses of Inductors
Switching power supplies
Power supply filtering
Transformers (coupled inductors)

## Slide 19: Diodes
One way gates for current
Open circuit in reverse direction
Constant 0.7V drop in forward direction (major simplification)

## Slide 20: Examples

## Slide 21: LEDs
Light Emitting Diodes
Behave a lot like standard diodes
Voltage drop is dependent on type of LED
1.5V to 4V drop typical (check datasheet)
Typically pass 20mA at forward voltage

## Slide 22: Current-limiting an LED

## Slide 23: Voltage Regulators
Output a constant, fixed voltage from an input voltage (usually higher)
Used as power supplies
TL7805 for example provides 5V regulated output
Essentially a self-varying
resistor

## Slide 24: Op-Amps
Operational Amplifiers take an input voltage and amplify it for a larger output voltage
This is a class onto itself

## Slide 25: Relays
Electrically actuated switches
Useful for switching AC and high currents
Slow and wasteful

## Slide 26: Transistors
BJTs and MOSFETs
Electrically actuated switches
Also used as amplifiers
The fundamental component of the computer revolution

## Slide 27: Transistor Application Circuits